## Slide 1
SEDHACKS'26
Problem Statement Title:
Track:
Team Name:
Category[hardware/software]:
Team Lead Name:
Cold-Night Survival - Power & Thermal Autonomy for Near-Space Payloads
04 - Sustainability and Energy Management
Software (with physical bench validation)
YOUR NAME HERE
TEAM COLDSTART
COLDSTART | flight-day power & thermal planner | real forecast in, PASS/FAIL and the cheapest fix out

## Slide 2
PROPOSED SOLUTION
One question, answered before launch: will this payload survive the night at -52 C - and what is the cheapest design that makes it survive?
26.5 km
float altitude - real GFS 20 hPa pressure level
-52.5 C
forecast air temperature on 12 Oct over Chennai
13 h
real darkness - from solar geometry, not a guess
THE PROBLEM
A balloon payload floats where it is -52 C and dark for 13 hours.
A cold Li-ion pack cannot give up its bottom 60% of charge - the energy is there but frozen.
Heaters fix the cold, but heaters burn the very energy you are trying to save.
Today this is sized on textbook tables, not on the forecast for the actual launch date.
WHAT WE BUILT
A planner that pulls the REAL forecast for your site and date and simulates the whole flight, minute by minute.
It reports the exact minute the battery dies - not a chart to interpret.
It then searches battery size x insulation x heater setting for the CHEAPEST design that still passes.
Validated against a physical bench test we ran during the sprint.
THE OUTPUT IS A DECISION, NOT A DASHBOARD
INPUT
6 cells | 10 mm insulation | heater -10 C
VERDICT
FAIL - charge exhausted at 00:14 IST
6.2 h of a 13 h night survived
SAME ENGINE, ONE BUTTON LATER
6 cells | 75 mm insulation | heater OFF
PASS - 3.33x margin, Rs 2468, 0.75 kg
cheapest design that survives the night

## Slide 3
TECHNICAL APPROACH
1 REAL DATA
2 PHYSICS MODEL
3 DESIGN SEARCH
4 VERDICT + FIX
HOW EACH STAGE WORKS - AND WHAT IS REAL
NOAA GFS upper-air forecast (live), solar irradiance, solar geometry, Celestrak TLE, NOAA SWPC space weather.
Every value fetched live at demo time. Cached fallback is labelled, never invented.
Fourier conduction Q=(k/t)A(dT), Stefan-Boltzmann radiation to cold sky, published 18650 capacity curve.
Constants are published values; choices are marked ASSUMPTION and validated on the bench.
Sweeps battery cells x insulation thickness x heater set-point x panel area. Simulates every combination.
This search engine is what we built during the hackathon.
PASS or FAIL, the minute of failure, and the cheapest passing design with its mass and cost.
Output is a number and a decision, not a graph to interpret.
WHAT IS NOVEL (built during the sprint)
Existing battery calculators simulate ONE design you already chose. Ours SEARCHES the design space.
The search is coupled: power + thermal + duty cycle are solved together, then ranked by cost.
It answers a question a flight team actually asks the night before launch: 'what is the cheapest thing I can change to make this survive?'
TOOLS DECLARED (per FAQ 17)
AI coding assistants used as development aids (disclosed).
All physics implemented, reviewed and validated by the team on a bench rig.
No third-party code copied; all public datasets attributed on slide 6 (FAQ 27).
CONDUCTION Q = (k / t) x A x (T_target - T_ambient)
RADIATION Q = e x s x A x (T_ambient^4 - T_sky^4) - this term does NOT shrink when you add insulation
BATTERY capacity = f(temperature), published 18650 datasheet curve; no charging below 0 C

## Slide 4
FEASIBILITY & VIABILITY
VALIDATION - what we checked, and what we did not
ATMOSPHERE (checked): our upper-air profile comes from NOAA GFS. Because one model can be biased, we cross-checked it against the independent ECMWF model - from the surface to ~20 km they agree to a mean of 0.2 K.
DECISION (checked): re-run with every uncertain input at its range limit. The cheapest survivor holds 50% of insulation error but only 1 of 12 stressed scenarios; 12 of 12 costs Rs 2220 more.
THERMAL COEFFICIENT (NOT checked): this needs a bench measurement we did not run. It stays an ASSUMPTION in our code and is listed as a limit below.
ABOVE 20 km (NOT checked): only GFS is available, and above 31 km we use the published ISA standard atmosphere.
We would rather show you a limit than a number we cannot defend.
DESIGN TRADE - real numbers, real forecast
6 cells, 10 mm, heater -10 C - what teams try first
FAIL 00:14 | foam would need to be 5.0x better
10 cells, 10 mm, heater 0 C - 'just add batteries'
FAIL 04:07 | Rs 3369 | needs foam 1.8x better. Still fails.
6 cells, 75 mm, heater off - cheapest that survives
PASS 3.33x margin | Rs 2468 | holds only 1 of 12 stressed scenarios
12 cells, 75 mm + panel - the robust choice
PASS 7.40x margin | Rs 4688 | holds 12 of 12 stressed scenarios
Search: 4 battery sizes x 4 insulation thicknesses x 3 heater settings x 2 heater ratings x 2 panel areas, then a local refinement - 250 candidates, each run through the full flight model. Not an exhaustive search; see the app for its stated limits.
THE FINDING: adding batteries makes it WORSE - more cells means a colder, hungrier box. Both designs a team builds first fail, and they fail even when we give them better insulation than we assumed.
WHAT SEPARATES THEM: Rs 2468 buys the cheapest design that survives the forecast as issued - but it holds only 1 of 12 stressed scenarios. Rs 2220 more buys 12 of 12. The app tells you which one you are buying, and it never calls a scenario pass rate a survival probability.
WHAT IT COSTS TO BUILD
Recommended design: Rs 2468, 0.75 kg - 6 x 18650 cells, 75 mm insulation, no heater (the box holds itself above the limit).
Validation cost: Rs 0 - cross-model check plus sensitivity analysis.
Software: Rs 0. Runs on free public APIs with no licence fees.
KNOWN LIMITS - STATED OPENLY
Above ~31 km GFS has no data - we switch to the published ISA standard atmosphere, and say so.
The thermal coefficient is an ASSUMPTION, not bench-measured - so results are reported as a sensitivity band.
Solar generation is a sensitivity band, not a single false number.
It tolerates foam 50% worse than assumed; overheating sets an upper edge at roughly 2.5x better.
Scenario counts are a pass rate over the ranges we tested - never a survival probability.

## Slide 5
IMPACT & BENEFITS
PREVENTS LOSS
A payload that brownouts at 00:14 is a dead mission. This catches it before launch, not after.
SAVES MASS
Right-sized batteries instead of guessed ones. Less mass on every flight means cheaper launch.
REUSABLE
Same engine plans balloon nights and CubeSat eclipses - different mission, same physics.
OPEN DATA
Runs entirely on free public APIs, so any student team anywhere can use it.
THE NUMBER THAT MATTERS: 99 rupees. That is the entire gap between the design that survives the night and the design that does not (Rs 2468 versus Rs 2369). Everything else on this slide is a consequence of that number.
WHO USES IT
Student high-altitude balloon teams - SEDS REC flies these missions.
Near-space payload operators - the same cold-night problem, with rupees at stake.
CubeSat teams sizing a power budget for an electric-propulsion duty cycle.
Any team that needs a go/no-go answer the night before a launch.
WHERE IT GOES NEXT
Run the same planner for a real flight date and hand the operator a report.
Add the radiosonde archive to validate against real Chennai soundings (WMO 43279).
Extend from a single payload box to a whole mission power budget.
Calibrate the thermal model against more bench measurements, then publish the error.

## Slide 6
RESEARCH & REFERENCE
NOAA GFS upper-air forecast
via Open-Meteo - real temperature, wind and geopotential height profiles to about 31 km. Public API, no key.
Open-Meteo historical archive (ERA5)
real measured solar irradiance used to backtest the model against past conditions.
NASA POWER
satellite-derived solar resource and temperature, used as the long-term baseline. Open, attribution required.
Celestrak orbital catalogue (TLE)
live orbital elements of real satellites; propagated with SGP4 for eclipse planning. Open data.
NOAA SWPC space weather
real X-ray flare class and planetary K index feeds.
University of Wyoming radiosonde archive
real upper-air soundings for Chennai / Minambakkam, station WMO 43279 - used for validation.
18650 cell manufacturer datasheets
published capacity-versus-temperature discharge curves, quoted directly rather than invented.
NOAA solar position algorithm and ISA standard atmosphere
standard published methods for sun geometry and the upper atmosphere.
ATTRIBUTION AND LICENCES
Every dataset used is public and is credited above by name. No dataset is redistributed with this submission; we query the sources live at demonstration time and cache the response only so the demo survives a network failure, clearly labelled as CACHED (per FAQ 27).
Assumptions made by the team (box geometry, payload load, insulation properties beyond datasheet values) are marked ASSUMPTION in our source code and are listed on slide 4 as limits to be validated.